## Slide 1: Flexible Body Examples on File Exchange
Lumped parameter beam
  Chain of mass-spring-dampers
Finite element import beam
  Superimpose bending onto rigid body motion
fileexchange/47051-flexible-body…

## Slide 2: Flexible Bodies in Simscape Multibody Approaches
UNDEFORMED BODY
F
F
F
J
W
J
STATE-SPACE SYSTEM
F
F
F
Weld Joint
Forces
Forces
Motion
Motion
F1
F3
F2
Lumped parameter approach
  Chain of rigid body-spring-dampers
  No finite element software required
  Only for simple geometries
    Stiffness value calculation
FEA Approach
  Export mass and stiffness matrices from FE software
  Superimpose deflection onto rigid body motion
  Valid for small deflections
Rigid Body
Rigid Body
Rigid Body
Finite Element Software

## Slide 3: Lumped Parameter Approach Generalized Flexible Element
Joint primitives reflect flexible degrees of freedom
  Bend: 1 rotational
  Bend+twist: 2 rotational
  Bend+stretch: 1 rotational + 1 prismatic
Use MATLAB to automate construction of flexible body
Element

## Slide 4: Basic Approach
Flexible-body deflection behavior modeled in Simulink is superimposed on the rigid-body motion modeled in Simscape Multibody
J
J
UNDEFORMED BODY
F
F
F
J
W
J
STATE-SPACE SYSTEM
F
F
F
F1
F2
F3
Weld Joint
Forces
Forces
Motion
Motion
F1
F3
F2

## Slide 5: Flexible Body Modeling Workflow
Create FE model in FEA software
Define part interface
Extract reduced order model
Import data into Simscape Multibody
Connect joints, forces, etc.
Simulate
CAD
FEA
N1
N2
FEA
Data
1
2
3
4
5
6
Notes: To model the flexibility of the wing in the context of the multibody simulation, using a Finite Element Import approach, CLICK we start with the creation of a finite element model of the wing.
CLICK Appropriate nodes are added to represent the connection points of the deformable body to other elements of the larger system.
CLICK A substructure characterizing the component’s structural behavior is generated based on the defined interface. Data for this reduced order model is stored in a file.
CLICK The data file is read to create the corresponding flexible body in the multibody system.
CLICK It is then integrated with the rest of the system, through joints, constraints, force elements, and more.
CLICK And finally, the model can be simulated and subsequently visualized and analyzed to solve the engineering problem.
CLICK

## Slide 6: Building the Flexible Body Subsystem Block
Create undeformed body
Add deflection joints
Replace one joint with a weld
Add connection ports for interface frames
Add state-space flexibility model
Set actuation mode for joints
Connect state-space output to force inputs
Connect sensed motion to state-space input
Break algebraic loops with filters
Encapsulate in a subsystem
Add interface frame masses and inertias

## Slide 7: Step 1 – Create Undeformed Body
Interface frames at boundary node locations of undeformed body
F1
F2
F3

## Slide 8: Step 2 – Add Deflection Joints
Bushing joints offer the required 6 dofs
J
J
F1
F3
J
F2
* prismatic joints shown for simplicity

## Slide 9: Step 3 – Replace One Joint With a Weld
Rigid-body modes in C-B model must be removed
Zero deformation at weld joint interface frame

## Slide 10: Step 4 – Add Connection Ports for Interface Frames
Expose interface frame ports on enclosing subsystem block
J
J
F1
F2
F3

## Slide 11: Step 5 – Add State-Space Flexibility Model
A, B, C, D matrices derived from reduced model equations

## Slide 12: Step 6 – Set Actuation Mode for Joints
Force: Provided by Input
Motion: Automatically Computed
* only position outputs shown for simplicity

## Slide 13: Step 7 – Connect State-Space Output to Force Inputs
State-space force outputs actuate deflection joints

## Slide 14: Step 8 – Connect Sensed Motion to State-Space Input
Sensed deflection joint motions used to compute appropriate forces

## Slide 15: Step 9 – Break Algebraic Loops with Filters
Direct feedthrough in SS system (D matrix) and SM mechanism (accel/force)

## Slide 16: Step 10 – Encapsulate in a Subsystem
Block can be used modularly

## Slide 17: Step 11 – Add Interface Frame Masses and Inertias
Best practice: non-zero effective mass and inertia at every moving frame
Small masses and inertias can hurt numerical stability

## Slide 18: High-Level Modeling Procedure for Using the Block
Choose a reference frame for the flexible body
Create CAD and FEA models
If necessary, add 6-dof nodes to the FE model
Choose the connection points for the multibody system
Generate the Craig-Bampton reduced model
Generate other required data
Add the flexible body block to the multibody system

## Slide 19: Step 1 – Choose a Reference Frame for the Flexible Body
Reference frame should be consistent between the different models:
  CAD model
  FEA model
  Multibody model
Frame with respect to which:
  Coordinates of points on body are defined
  Deformations are measured

## Slide 20: Step 2 – Create CAD and FEA Models
Reference frame consistent between various models
CAD Model
FEA Model

## Slide 21: Step 3 – If Necessary, Add 6-Dof Nodes to the FE Model
For compatibility with the multibody system, the FEA substructure must have 6-dof nodes
  3-D beam or shell elements
  Individual 6-dof nodes, properly constrained to other nodes
Spider
Rigid
Region

## Slide 22: Step 4 – Choose the Connection Points for the Multibody System
For attaching joints, bodies, constraints, forces, etc.
For visualization, sensing, etc.
Ordering must be consistent between all data structures
F1
F2
F3

## Slide 23: Step 5 – Generate the Craig-Bampton Reduced Model
To create the substructure, select:
  Nodes to retain
  Number of dynamic vibration modes to include
This process generates:
  Reduced mass matrix M
  Reduced stiffness matrix K
  Optionally, a recovery matrix (not needed for simulation)

## Slide 24: Step 6 – Generate Other Required Data
Other data derived from the CAD and FEA models:
  CAD file in STL or STEP format
  Array of interface frame coordinates
  Inertia properties of the undeformed body (mass, com, moi, poi)
Array mapping interface frame indices to dof indices in reduced dof vector
  May be trivial if order matches in C-B substructure and multibody system

## Slide 25: Step 7 – Add the Flexible Body Block to the Multibody System
Additional parameters may be required:
  Simulation:
    Filtering constant to break algebraic loops
    Mass and inertia at the interface frames
  Visualization:
    Approximate in nature, so may need tweaking

## Slide 26: Other Topics – Mass at Interface Frames
Since deflections are modeled through joints, degenerate mass errors can occur if the interface frames of the flexible body are directly connected to other joints or other elements such as constraints, forces, etc.
To address the issue
  Use small negligible masses and inertias (how to pick sizes?)
  Attach small but meaningful masses and inertias that represent something physical
  Divide body into bigger chunks – mass and inertia are more evenly distributed

## Slide 27: Other Topics – Mass at Interface Frames
Use small negligible masses and inertias
  Does not correspond to any meaningfully modeled aspect of the system
  Small enough to have negligible effect on the dynamics
  Large enough to avoid degenerate mass errors or slowness of simulation

## Slide 28: Other Topics – Mass at Interface Frames
Attach small but meaningful masses and inertias that represent something physical: collars, pins, connectors, part ends, etc.
Rigid Pieces
Rigid Pieces
Modeled as
Flexible Body
Modeled as
Flexible Body

## Slide 29: Other Topics – Mass at Interface Frames
Model the entire part as a flexible body
But divide mass and inertia into chunks (mass more evenly distributed)
Entire Body
Modeled as
Flexible Body
Rigid Body Inertia
Split Between
Interface Frames

## Slide 30: Other Topics – Visualization
For larger deformations
  Quality of visualization decreases (only undeformed body is shown)
  Visualization can be misleading (depends on undeformed body attachment frame)